## Slide 1: I/O PORTS

## Slide 2: I/O PORTS
The 8051 has four I/O ports
  Port 0 （pins 32-39）：P0（P0.0～P0.7）
  Port 1（pins 1-8） ：P1（P1.0～P1.7）
  Port 2（pins 21-28）：P2（P2.0～P2.7）
  Port 3（pins 10-17）：P3（P3.0～P3.7）
  Each port has 8 pins.
    Named P0.X, P1.X, P2.X, P3.X （X=0,1,...,7）
    Ex：P0.0 is the bit 0（LSB）of P0
    Ex：P0.7 is the bit 7（MSB）of P0
    These 8 bits form a byte.
Each port can be used as input or output (bi-direction).

## Slide 4: PORT0
When used as input, a ‘1’ must be written to corresponding port latch
Used as an output,’0’ must be programmed
Logic ‘1’ in address bit will turn Upper FET on & lower FET off
After address has formed & latched into External circuitry by ALE pulse, the External Bus is turned ON
Port 0 now reads data from External Memory
Port 0 pins can be accessed by address P0.0,P0.1,….,P0.7
It can also be addressed as AD0,AD1,…….AD7

## Slide 5: PORT1
Port 1 pins have no Dual functions
If used as input a ‘1’ is written to latch which turns upper FET on
Used as output,lower FET is On & the Pullup is Off
Output latch is directly connected to gate of Lower FET
Port 1 can be accessed as P1.0,P1.1,. . . . .P1.7

## Slide 6: PORT2
It can be used as I/p or o/p which is similar in operation of Port 1
The alternate use of port 2 is to supply a high-order address byte in conjunction with port 0 low-order byte to address external memory
Port 2 latches remain stable when External Memory is addressed
They do not have to be turned around (Set to 1) For Data i/p as in Port 0
It can be accessed as P2.0,P2.1,. . . . . ,P2.7

## Slide 7: PORT3
It is similar to port 1,but has alternate Uses
Each pin may be individually Programmed as I/O or for alternate Functions as shown
Pin | Alternate Use SFR
P3.0-RXD | Serial data input SBUF
P3.1-TXD | Serial data Output SBUF
P3.2-INT0 | External interrupt 0 TCON.1
P3.3-INT1 | External interrupt 1 TCON.3
P3.4-T0 | External timer 0 input TMOD
P3.5-T1 | External timer 1 input TMOD
P3.6-WR | External Memory Write Pulse -
P3.7-RD | External Memory Read Pulse -

## Slide 8: A Pin of Port 1
8051 IC
D Q
Clk Q
Vcc
Load(L1)
Read latch
Read pin
Write to latch
Internal CPU bus
M1
P1.X pin
P1.X
TB1
TB2
P1.x

## Slide 9: Hardware Structure of I/O Pin
Each pin of I/O ports
  Internal CPU bus：communicate with CPU
  A D latch store the value of this pin
    D latch is controlled by “Write to latch”
      Write to latch＝1：write data into the D latch
  2 Tri-state buffer：
    TB1: controlled by “Read pin”
      Read pin＝1：really read the data present at the pin
    TB2: controlled by “Read latch”
      Read latch＝1：read value from internal latch
  A transistor M1 gate
    Gate=0: open
    Gate=1: close

## Slide 10: Tri-state Buffer
Output
Input
Tri-state control (active high)
L
H
Low
Highimpedance (open-circuit)
H
H
L
H

## Slide 11: Writing “1” to Output Pin P1.X
D Q
Clk Q
Vcc
Load(L1)
Read latch
Read pin
Write to latch
Internal CPU bus
M1
P1.X pin
P1.X
8051 IC
2. output pin is Vcc
1. write a 1 to the pin
1
0
output 1
TB1
TB2

## Slide 12: Writing “0” to Output Pin P1.X
D Q
Clk Q
Vcc
Load(L1)
Read latch
Read pin
Write to latch
Internal CPU bus
M1
P1.X pin
P1.X
8051 IC
2. output pin is ground
1. write a 0 to the pin
0
1
output 0
TB1
TB2

## Slide 13: Port 1 as Output（Write to a Port）
Send data to Port 1：
  MOV A,#55H
  BACK: MOV P1,A
  ACALL DELAY
  CPL A
  SJMP BACK
  Let P1 toggle.
  You can write to P1 directly.

## Slide 14: Reading Input v.s. Port Latch
When reading ports, there are two possibilities：
  Read the status of the input pin. （from external pin value）
    MOV A, PX
    JNB P2.1, TARGET ; jump if P2.1 is not set
    JB P2.1, TARGET ; jump if P2.1 is set
  Read the internal latch of the output port.
    ANL P1, A ; P1 ← P1 AND A
    ORL P1, A ; P1 ← P1 OR A
    INC P1 ; increase P1

## Slide 15: Reading “High” at Input Pin
D Q
Clk Q
Vcc
Load(L1)
Read latch
Read pin
Write to latch
Internal CPU bus
M1
P1.X pin
P1.X
8051 IC
2. MOV A,P1
external pin=High
write a 1 to the pin MOV P1,#0FFH
1
0
3. Read pin=1 Read latch=0 Write to latch=1
1
TB1
TB2